## Slide 1: Data and Computer Communications
Ninth Edition
by William Stallings
Chapter 10 – Circuit Switching and Packet Switching
Notes: “Data and Computer Communications”, 9/e, by William Stallings, Chapter 10 “Circuit Switching and Packet Switching”.

## Slide 2: Circuit Switching and Packet Switching
He got into a District Line train at Wimbledon Park, changed on to the Victoria Line at Victoria and on to the Jubilee Line at Green Park for West Hampstead. It was a long and awkward journey but he enjoyed it.
—King Solomon's Carpet,
Barbara Vine (Ruth Rendell)
Notes: This quote is from the start of Stallings DCC9e Ch10 hints at the issue of choosing an appropriate path for information to flow over through a network. The chapter begins with a general discussion of switched communications networks. The remainder of the chapter focuses on wide area networks and, in particular, on traditional approaches to wide area network design: circuit switching and packet switching.

## Slide 3: Switched Communications Networks
switching nodes provide a switching facility that move data between nodes
  stations – devices attached to the network
  nodes – switching devices that provide communication
    connected by transmission links
    dedicated point-to-point
    usually multiplexed using either FDM or TDM
Notes: For transmission of data beyond a local area, communication is typically achieved by transmitting data from source to destination through a network of intermediate switching nodes; this switched network design is typically used to implement LANs as well. The switching nodes are not concerned with the content of the data; rather, their purpose is to provide a switching facility that will move the data from node to node until they reach their destination.
The devices attached to the network may be referred to as stations. The stations may be computers, terminals, telephones, or other communicating devices. We refer to the switching devices whose purpose is to provide communication as nodes. Nodes are connected to one another in some topology by transmission links. Node-station links are generally dedicated point-to-point links. Node-node links are usually multiplexed, using either frequency division multiplexing (FDM) or time division multiplexing (TDM).

## Slide 4: Switched Network
Notes: Stallings DCC9e Figure 10.1 illustrates a simple network. In a switched communication network, data entering the network from a station are routed to the destination by being switched from node to node. For example, in Figure 10.1, data from station A intended for station F are sent to node 4. They may then be routed via nodes 5 and 6 or nodes 7 and 6 to the destination.

## Slide 5: (Communication Networks)
in addition to switching functions, some nodes also deliver data to attached stations
network is not fully connected so there is not a direct link between every possible pair of nodes
switching technologies:
circuit switching
packet switching
communication network :
a collection of nodes
redundant connections increase network reliability
Notes: Each station attaches to a node, and the collection of nodes is referred to as a communications network. Some nodes have stations attached as well; in addition to their switching functions, such nodes accept data from and deliver data to the attached stations. Usually, the network is not fully connected; that is, there is not a direct link between every possible pair of nodes. However, it is always desirable to have more than one possible path through the network for each pair of stations. This enhances the reliability of the network.
Two different technologies are used in wide area switched networks: circuit switching and packet switching. These two technologies differ in the way the nodes switch information from one link to another on the way from source to destination.

## Slide 6: Circuit Switching
uses a dedicated path between two stations
can be inefficient
  channel capacity dedicated for duration of connection
  if no data, capacity wasted
set up (connection) takes time
once connected, transfer is transparent
has three phases
establish
transfer
disconnect
Notes: Communication via circuit switching implies that there is a dedicated communication path between two stations. That path is a connected sequence of links between network nodes. On each physical link, a logical channel is dedicated to the connection. Communication via circuit switching involves three phases:
Circuit establishment - Before any signals can be transmitted, an end-to-end (station-to-station) circuit must be established.
Data transfer - Data can now be transmitted through the network between these two stations. The transmission may be analog or digital, depending on the nature of the network. As the carriers evolve to fully integrated digital networks, the use of digital (binary) transmission for both voice and data is becoming the dominant method. Generally, the connection is full duplex.
Circuit disconnect - After some period of data transfer, the connection is terminated, usually by the action of one of the two stations. Signals must be propagated to the intermediate nodes to deallocate the dedicated resources.
Circuit switching can be rather inefficient. Channel capacity is dedicated for the duration of a connection, even if no data are being transferred. For a voice connection, utilization may be rather high, but it still does not approach 100%. For a client/server or terminal-to-computer connection, the capacity may be idle during most of the time of the connection. In terms of performance, there is a delay prior to signal transfer for call establishment. However, once the circuit is established, the network is effectively transparent to the users.

## Slide 7: (Public Telecommunications Network)
examples of circuit switching network:
Public telephone network
subscribers –
devices that attach to the network
subscriber line –
link subscriber and network
Private branch exchange (PBX)
interconnects telephones within a building
exchanges –
switching centers in network
trunks –
branches between exchanges
Data switch
Interconnects digital data processing devices such as terminals and computers
Notes: The best-known example of a circuit-switching network is the public telephone network. This is actually a collection of national networks interconnected to form the international service. A public telecommunications network can be described using four generic architectural components:
• Subscribers: The devices that attach to the network, typically telephones, but the percentage of data traffic increases year by year.
• Subscriber line: The link between the subscriber and the network, also referred to as the subscriber loop or local loop, mostly using twisted-pair wire.
• Exchanges: The switching centers in the network. A switching center that directly supports subscribers is known as an end office.
Trunks: The branches between exchanges. Trunks carry multiple voice-frequency circuits using either FDM or synchronous TDM

## Slide 8: Public Circuit Switched Network
Notes: Circuit switching was developed to handle voice traffic but is now also used for data traffic. (see Stallings DCC9e Figure 10.2 above).

## Slide 9: (Circuit Establishment)
Notes: Subscribers connect directly to an end office, which switches traffic between subscribers and between a subscriber and other exchanges. The other exchanges are responsible for routing and switching traffic between end offices. This distinction is shown here in Stallings DCC9e Figure 10.3. To connect two subscribers attached to the same end office, a circuit is set up between them. If two subscribers connect to different end offices, a circuit between them consists of a chain of circuits through one or more intermediate offices. In the figure, a connection is established between lines a and b by simply setting up the connection through the end office. The connection between c and d is more complex. In c's end office, a connection is established between line c and one channel on a TDM trunk to the intermediate switch. In the intermediate switch, that channel is connected to a channel on a TDM trunk to d's end office. In that end office, the channel is connected to line d.

## Slide 10: (Circuit-Switching Technology)
Driven by applications that handle voice traffic
  Key requirement is no transmission delay and no variation in delay
Efficient for analog transmission of voice signals
Inefficient for digital transmission
Transparent
  once a circuit is established it appears as a direct connection; no special logic is needed
Notes: Circuit-switching technology has been driven by those applications that handle voice traffic. One of the key requirements for voice traffic is that there must be virtually no transmission delay and certainly no variation in delay. A constant signal transmission rate must be maintained, because transmission and reception occur at the same signal rate. These requirements are necessary to allow normal human conversation. Further, the quality of the received signal must be sufficiently high to provide, at a minimum, intelligibility. Circuit switching achieved its widespread, dominant position because it is well suited to the analog transmission of voice signals. In today's digital world, its inefficiencies are more apparent. However, despite the inefficiency, circuit switching will remain an attractive choice for both local area and wide area networking.

## Slide 11: (Circuit-Switching Concepts) (see next slide…)
digital switch
provides a transparent signal path
must allow full-duplex transmission
network interface
functions and hardware needed to connect digital devices
control unit
establishes, maintains, and tears down the connection
Notes: The heart of a modern system is a digital switch. The function of the digital switch is to provide a transparent signal path between any pair of attached devices. The path is transparent in that it appears to the attached pair of devices that there is a direct connection between them. Typically, the connection must allow full-duplex transmission.
The network interface element represents the functions and hardware needed to connect digital devices, such as data processing devices and digital telephones, to the network. Analog telephones can also be attached if the network interface contains the logic for converting to digital signals. Trunks to other digital switches carry TDM signals and provide the links for constructing multiple-node networks.
The control unit performs three general tasks. First, it establishes connections. This is generally done on demand, that is, at the request of an attached device. Second, the control unit must maintain the connection. Because the digital switch uses time division principles, this may require ongoing manipulation of the switching elements. Third, the control unit must tear down the connection, either in response to a request from one of the parties or for its own reasons.

## Slide 12: (Circuit Switch Elements)
Notes: The technology of circuit switching is best approached by examining the operation of a single circuit-switching node. A network built around a single circuit-switching node consists of a collection of stations attached to a central switching unit. The central switch establishes a dedicated path between any two devices that wish to communicate. Stallings DCC9e Figure 10.4 depicts the major elements of such a one-node network. The dotted lines inside the switch symbolize the connections that are currently active.

## Slide 13: (Blocking or Non-blocking)
blocking network
  may be unable to connect stations because all paths are in use
  used on voice systems because it is expected for phone calls to be of short duration and that only a fraction of the phones will be engaged at any one time
non-blocking network
  permits all stations to connect at once
  grants all possible connection requests as long as the called party is free
  when using data connections, terminals can be continuously connected for long periods of time so nonblocking configurations are required
Notes: An important characteristic of a circuit-switching device is whether it is blocking or nonblocking. Blocking occurs when the network is unable to connect two stations because all possible paths between them are already in use. A blocking network is one in which such blocking is possible. Hence a nonblocking network permits all stations to be connected (in pairs) at once and grants all possible connection requests as long as the called party is free. When a network is supporting only voice traffic, a blocking configuration is generally acceptable, because it is expected that most phone calls are of short duration and that therefore only a fraction of the telephones will be engaged at any time. However, when data processing devices are involved, these assumptions may be invalid. For example, for a data entry application, a terminal may be continuously connected to a computer for hours at a time. Hence, for data applications, there is a requirement for a nonblocking or "nearly nonblocking" (very low probability of blocking) configuration.

## Slide 14: (Space Division Switching)
originally developed for analog, space division switching has been carried over into the digital realm
signal paths are physically separate from one another
path is dedicated solely to transfer signals
basic building block of switch is a metallic crosspoint or semiconductor gate
Notes: We turn now to an examination of the switching techniques internal to a single circuit-switching node. Space division switching was originally developed for the analog environment and has been carried over into the digital realm. A space division switch is one in which the signal paths are physically separate from one another (divided in space). Each connection requires the establishment of a physical path through the switch that is dedicated solely to the transfer of signals between the two endpoints. The basic building block of the switch is a metallic crosspoint or semiconductor gate that can be enabled and disabled by a control unit.

## Slide 15: (Space Division Switch)
Notes: Stallings DCC9e Figure 10.5 shows a simple crossbar matrix with 10 full-duplex I/O lines. The matrix has 10 inputs and 10 outputs; each station attaches to the matrix via one input and one output line. Interconnection is possible between any two lines by enabling the appropriate crosspoint. Note that a total of 100 crosspoints is required. The crossbar switch has a number of limitations:
•The number of crosspoints grows with the square of the number of attached stations. This is costly for a large switch.
•The loss of a crosspoint prevents connection between the two devices whose lines intersect at that crosspoint.
•The crosspoints are inefficiently utilized; even when all of the attached devices are active, only a small fraction of the crosspoints are engaged.

## Slide 16: (3 Stage Space Division Switch)
Notes: To overcome these limitations, multiple-stage switches are employed. Stallings DCC9e Figure 10.6 is an example of a three-stage switch. This type of arrangement has two advantages over a single-stage crossbar matrix:
•The number of crosspoints is reduced, increasing crossbar utilization. In examples 10.2 and 10.3 the total number of crosspoints for 10 stations is reduced from 100 to 48.
•There is more than one path through the network to connect two endpoints, increasing reliability.
Of course, a multistage network requires a more complex control scheme. To establish a path in a single-stage network, it is only necessary to enable a single gate. In a multistage network, a free path through the stages must be determined and the appropriate gates enabled. A consideration with a multistage space division switch is that it may be blocking. It should be clear from Stallings DCC9e Figure 10.5 that a single-stage crossbar matrix is nonblocking; that is, a path is always available to connect an input to an output. That this may not be the case with a multiple-stage switch can be seen in Stallings DCC9e Figure 10.6. The heavier lines indicate the lines that are already in use. In this state, input line 10, for example, cannot be connected to output line 3, 4, or 5, even though all of these output lines are available. A multiple-stage switch can be made nonblocking by increasing the number or size of the intermediate switches, but of course this increases the cost.

## Slide 17: (Time Division Switching)
modern digital systems use intelligent control of space & time division elements (i.e. they use TDM and space division)
use digital time division techniques to set up and maintain virtual circuits
partition low speed bit stream into pieces that share higher speed stream
individual pieces manipulated by control logic to flow from input to output
Notes: The technology of switching has a long history, most of it covering an era when analog signal switching predominated. With the advent of digitized voice and synchronous time division multiplexing techniques, both voice and data can be transmitted via digital signals. This has led to a fundamental change in the design and technology of switching systems. Instead of relatively dumb space division systems, modern digital systems rely on intelligent control of space and time division elements.
Virtually all modern circuit switches use digital time division techniques for establishing and maintaining "circuits." Time division switching involves the partitioning of a lower-speed bit stream into pieces that share a higher-speed stream with other bit streams. The individual pieces, or slots, are manipulated by control logic to route data from input to output. There are a number of variations on this basic concept, which are beyond the scope of this book

## Slide 18: (Softswitch Architecture)
latest trend in circuit-switching technology
computer running specialized software that turns it into a smart phone switch (not a “smartphone” switch…)
costs less and provides more functionality (allows voice over IP…)
Media gateway (MG) – physical switching
Media gateway controller (MGC) – call processing logic
Notes: The latest trend in the development of circuit-switching technology is generally referred to as the softswitch. In essence, a softswitch is a general-purpose computer running specialized software that turns it into a smart phone switch. Softswitches cost significantly less than traditional circuit switches and can provide more functionality. In particular, in addition to handling the traditional circuit-switching functions, a softswitch can convert a stream of digitized voice bits into packets. This opens up a number of options for transmission, including the increasingly popular voice over IP (Internet Protocol) approach.
In any telephone network switch, the most complex element is the software that controls call processing. This software performs call routing and implements call-processing logic for hundreds of custom calling features. Typically, this software runs on a proprietary processor that is integrated with the physical circuit-switching hardware. A more flexible approach is to physically separate the call processing function from the hardware switching function. In softswitch terminology, the physical switching function is performed by a media gateway (MG) and the call processing logic resides in a media gateway controller (MGC).

## Slide 19: (Traditional Circuit Switching)
Notes: Stallings DCC9e Figure 10.7a contrasts the architecture of a traditional telephone network circuit switch with the softswitch architecture. In the latter case, the MG and MGC are distinct entities and may be provided by different vendors. To facilitate interoperability, ITU-T has issued a standard for a media gateway control protocol between the MG and MGC: H.248.1 (Gateway Control Protocol, Version 3, 2005). RFC 2805 (Media Gateway Control Protocol Architecture and Requirements, 2000) provides an overview of media gateway concepts.

## Slide 20: (Softswitch) Ex: http://partners.varphonex.com/services/softswitch.php http://speedflow.com/index.php/en/services/softswitch-rent
Notes: Stallings DCC9e Figure 10.7b illustrates the softswitch architecture.

## Slide 21: Packet Switching
circuit switching was designed for voice
packet switching was designed for data
transmitted in small packets
packets contains user data and control info
  user data may be part of a larger message
  control information includes routing (addressing)
packets are received, stored briefly (buffered) and passed on to the next node
Notes: The long-haul circuit-switching telecommunications network was originally designed to handle voice traffic, and resources within the network are dedicated to a particular call. With increasing use of data communications its limitations become more apparent.
In contrast a packet-switching network is designed for data use. Data are transmitted in short packets. A typical upper bound on packet length is 1000 octets (bytes). If a source has a longer message to send, the message is broken up into a series of packets. Each packet contains a portion (or all for a short message) of the user's data plus some control information. The control information, at a minimum, includes the information that the network requires to be able to route the packet through the network and deliver it to the intended destination. At each node en route, the packet is received, stored briefly, and passed on to the next node.

## Slide 22: Packet Switching
Notes: Stallings DCC9e Figure 10.8 illustrates how a longer message is broken up into a series of packets, which are transferred over the packet-switched network.

## Slide 23: Advantages
line efficiency
  single link shared by many packets over time
  packets queued and transmitted as fast as possible
data rate conversion
  stations connects to local node at own speed
  nodes buffer data if required to equalize rates
packets accepted even when network is busy
priorities can be used
Notes: A packet-switching network has a number of advantages over circuit switching:
• Line efficiency is greater, because a single node-to-node link can be dynamically shared by many packets over time. The packets are queued up and transmitted as rapidly as possible over the link. By contrast, with circuit switching, time on a node-to-node link is preallocated using synchronous time division multiplexing. Much of the time, such a link may be idle because a portion of its time is dedicated to a connection that is idle.
• A packet-switching network can perform data-rate conversion. Two stations of different data rates can exchange packets because each connects to its node at its proper data rate.
• When traffic becomes heavy on a circuit-switching network, some calls are blocked; that is, the network refuses to accept additional connection requests until the load on the network decreases. On a packet-switching network, packets are still accepted, but delivery delay increases.
• Priorities can be used. If a node has a number of packets queued for transmission, it can transmit the higher-priority packets first. These packets will therefore experience less delay than lower-priority packets.

## Slide 24: Switching Techniques
station breaks long message into packets
packets sent one at a time to the network
packets can be handled in two ways:
  datagram
    each packet is treated independently with no reference to previous packets
  virtual circuit
    a preplanned route is established before any packets are sent
Notes: If a station has a message to send through a packet-switching network that is of length greater than the maximum packet size, it breaks the message up into packets and sends these packets, one at a time, to the network. A question arises as to how the network will handle this stream of packets as it attempts to route them through the network and deliver them to the intended destination. Two approaches are used in contemporary networks: datagram and virtual circuit.

## Slide 25: Datagram Diagram
Notes: In the datagram approach, each packet is treated independently, with no reference to packets that have gone before. This approach is illustrated in Stallings DCC9e Figure 10.9, which shows a time sequence of snapshots of the progress of three packets through the network. Each node chooses the next node on a packet's path, taking into account information received from neighboring nodes on traffic, line failures, and so on. So the packets, each with the same destination address, do not all follow the same route, and they may arrive out of sequence at the exit point. In this example, the exit node restores the packets to their original order before delivering them to the destination. In some datagram networks, it is up to the destination rather than the exit node to do the reordering. Also, it is possible for a packet to be destroyed in the network. For example, if a packet-switching node crashes momentarily, all of its queued packets may be lost. Again, it is up to either the exit node or the destination to detect the loss of a packet and decide how to recover it. In this technique, each packet, treated independently, is referred to as a datagram.

## Slide 26: Virtual Circuit Diagram
Notes: In the virtual circuit approach, a preplanned route is established before any packets are sent. Once the route is established, all the packets between a pair of communicating parties follow this same route through the network. This is illustrated in Stallings DCC9e Figure 10.10. Because the route is fixed for the duration of the logical connection, it is somewhat similar to a circuit in a circuit-switching network and is referred to as a virtual circuit. Each packet contains a virtual circuit identifier as well as data. Each node on the preestablished route knows where to direct such packets; no routing decisions are required. At any time, each station can have more than one virtual circuit to any other station and can have virtual circuits to more than one station.
So the main characteristic of the virtual circuit technique is that a route between stations is set up prior to data transfer. Note that this does not mean that this is a dedicated path, as in circuit switching. A transmitted packet is buffered at each node, and queued for output over a line, while other packets on other virtual circuits may share the use of the line. The difference from the datagram approach is that, with virtual circuits, the node need not make a routing decision for each packet. It is made only once for all packets using that virtual circuit.

## Slide 27: Virtual Circuits vs. Datagram
virtual circuits
  network can provide sequencing and error control
  packets are forwarded more quickly
  less reliable
datagram
  no call setup phase
  more flexible
  more reliable
Notes: If two stations wish to exchange data over an extended period of time, there are certain advantages to virtual circuits. First, the network may provide services related to the virtual circuit, including sequencing and error control. Sequencing refers to the fact that, because all packets follow the same route, they arrive in the original order. Error control is a service that assures not only that packets arrive in proper sequence, but also that all packets arrive correctly. Another advantage is that packets should transit the network more rapidly with a virtual circuit; it is not necessary to make a routing decision for each packet at each node.
One advantage of the datagram approach is that the call setup phase is avoided. Thus, if a station wishes to send only one or a few packets, datagram delivery will be quicker. Another advantage of the datagram service is that, because it is more primitive, it is more flexible. For example, if congestion develops in one part of the network, incoming datagrams can be routed away from the congestion. With the use of virtual circuits, packets follow a predefined route, and thus it is more difficult for the network to adapt to congestion. A third advantage is that datagram delivery is inherently more reliable. With the use of virtual circuits, if a node fails, all virtual circuits that pass through that node are lost. With datagram delivery, if a node fails, subsequent packets may find an alternate route that bypasses that node. A datagram-style of operation is common in internetworks.

## Slide 28: Event Timing
Notes: A simple comparison of circuit switching and the two forms of packet switching is provided in Stallings DCC9e Figure 10.12. The figure depicts the transmission of a message across four nodes, from node 1 to 4.
For circuit switching, there is a delay before the message is sent. First, a Call Request signal is sent. If the destination station is not busy, a Call Accepted signal returns. Note a processing delay is incurred at each node during the call request. On return, this processing is not needed because the connection is already set up. After the connection is set up, the message is sent as a single block, with no noticeable delay at the switching nodes.
Virtual circuit packet switching appears similar to circuit switching. A virtual circuit is requested using a Call Request packet, which incurs a delay at each node, and is accepted with a Call Accept packet. In contrast to the circuit-switching case, the call acceptance also experiences node delays, since each packet is queued at each node and must wait its turn for transmission. Once the virtual circuit is established, the message is transmitted in packets. Packet switching involves some delay at each node in the path. Worse, this delay is variable and will increase with increased load.
Datagram packet switching does not require a call setup. Thus, for short messages, it will be faster than virtual circuit and perhaps circuit switching. However, because each individual datagram is routed independently, the processing at each node may be longer than for virtual circuit packets. For long messages virtual circuits may be superior.

## Slide 29: There is a significant relationship between packet size and transmission time
Notes: There is a significant relationship between packet size and transmission time, as shown in Stallings DCC9e Figure 10.11, which assumes a virtual circuit exists from station X through nodes a and b to station Y. The message to be sent comprises 40 octets, with 3 octets of control information at the beginning of each packet in the header. If the entire message is sent as a single packet of 43 octets (3 octets of header plus 40 octets of data), then the packet is first transmitted from station X to node a (Figure 10.11a). When the entire packet is received, it can then be transmitted from a to b. When the entire packet is received at node b, it is then transferred to station Y. Ignoring switching time, total transmission time is 129 octet-times (43 octets  3 packet transmissions).
If we break the message into two packets with 20 octets of message and 3 octets of header each. In this case, node a can begin transmitting the first packet as soon as it has arrived from X. Because of this overlap in transmission, the total transmission time drops to 92 octet-times. By breaking the message into five packets, each intermediate node can begin transmission even sooner, with a total of 77 octet-times for transmission. This process of using more and smaller packets eventually results in increased, rather than reduced, delay as illustrated in Figure 10.11d, since each packet contains a fixed amount of header, and more packets Also, processing and queuing delays at each node are greater when more packets are handled for a single message. However, we shall see in the next chapter that an extremely small packet size (53 octets) can result in an efficient network design.

## Slide 30: (Comparison of Communication Switching Techniques)
Notes: Stallings DCC9e Table 10.1 Comparison of Communication Switching Techniques

## Slide 31: (External Network Interface)
ITU-T standard for interface between host and packet switched network
almost universal on packet switched networks and packet switching
Ex. ISDN note: ISDN was displaced by ADSL…
Notes: One technical aspect of packet-switching networks remains to be examined: the interface between attached devices and the network. We have seen that a circuit-switching network provides a transparent communications path for attached devices that makes it appear that the two communicating stations have a direct link. However, in the case of packet-switching networks, the attached stations must organize their data into packets for transmission. This requires a certain level of cooperation between the network and the attached stations. This cooperation is embodied in an interface standard. The standard used for traditional packet-switching networks is X.25, which is an ITU-T standard that specifies an interface between a host system and a packet-switching network. The functionality of X.25 is specified on three levels: Physical level, Link level, and Packet level.

## Slide 32: ISDN networking
http://www.2n.cz/en/products/gsm-gateways/digital-isdn-bri/bri-enterprise/tech-specs/
http://www.cisco.com/c/en/us/products/collateral/routers/800-series-routers/product_data_sheet09186a008014ee18.html
Voice, video and data over public switched telephone network.
Offers circuit-switch connections for voice or data and packet-switched connections for data.
Notes: An example of X.25 virtual circuits is shown in Stallings DCC9e Figure 10.13 (compare Figure 10.1). In this example, station A has a virtual circuit connection to C; station B has two virtual circuits established, one to C and one to D; and stations E and F each have a virtual circuit connection to D. As an example of how these external virtual circuits are used, station D keeps track of data packets arriving from three different workstations (B, E, F) on the basis of the virtual circuit number associated with each incoming packet.
Typically, standards for packet-switching network interfaces define a virtual circuit service. This service enables any subscriber to the network to set up logical connections, called virtual circuits, to other subscribers. An example is shown in Figure 10.13 (compare Figure 10.1). In this example, station A has a virtual circuit connection to C; station B has two virtual circuits established, one to C and one to D; and stations E and F each have a virtual circuit connection to D.
In this context, the term virtual circuit refers to the logical connection between two stations through the network; this is perhaps best termed an external virtual circuit. Earlier, we used the term virtual circuit to refer to a specific preplanned route through the network between two stations; this could be called an internal virtual circuit. Typically, there is a one-to-one relationship between external and internal virtual circuits. However, it is also possible to employ an external virtual circuit service with a datagram-style network. What is important for an external virtual circuit is that there is a logical relationship, or logical channel, established between two stations, and all of the data associated with that logical channel are considered as part of a single stream of data between the two stations. For example, in Figure 10.13, station D keeps track of data packets arriving from three different workstations (B, E, F) on the basis of the virtual circuit number associated with each incoming packet.

## Slide 33: X.25 Networks (packet switched network)
X.25 defines three layers
  Physical (X.21) - (via adapters)
  Link
  Packet (X.25)
Notes: One technical aspect of packet-switching networks remains to be examined: the interface between attached devices and the network. We have seen that a circuit-switching network provides a transparent communications path for attached devices that makes it appear that the two communicating stations have a direct link. However, in the case of packet-switching networks, the attached stations must organize their data into packets for transmission. This requires a certain level of cooperation between the network and the attached stations. This cooperation is embodied in an interface standard. The standard used for traditional packet-switching networks is X.25, which is an ITU-T standard that specifies an interface between a host system and a packet-switching network. The functionality of X.25 is specified on three levels: Physical level, Link level, and Packet level.

## Slide 34: X.25 Use of Virtual Circuits (see http://www.advancedrelay.com/ci/images/solutions/x25-legacy-network.png)
Notes: An example of X.25 virtual circuits is shown in Stallings DCC9e Figure 10.13 (compare Figure 10.1). In this example, station A has a virtual circuit connection to C; station B has two virtual circuits established, one to C and one to D; and stations E and F each have a virtual circuit connection to D. As an example of how these external virtual circuits are used, station D keeps track of data packets arriving from three different workstations (B, E, F) on the basis of the virtual circuit number associated with each incoming packet.
Typically, standards for packet-switching network interfaces define a virtual circuit service. This service enables any subscriber to the network to set up logical connections, called virtual circuits, to other subscribers. An example is shown in Figure 10.13 (compare Figure 10.1). In this example, station A has a virtual circuit connection to C; station B has two virtual circuits established, one to C and one to D; and stations E and F each have a virtual circuit connection to D.
In this context, the term virtual circuit refers to the logical connection between two stations through the network; this is perhaps best termed an external virtual circuit. Earlier, we used the term virtual circuit to refer to a specific preplanned route through the network between two stations; this could be called an internal virtual circuit. Typically, there is a one-to-one relationship between external and internal virtual circuits. However, it is also possible to employ an external virtual circuit service with a datagram-style network. What is important for an external virtual circuit is that there is a logical relationship, or logical channel, established between two stations, and all of the data associated with that logical channel are considered as part of a single stream of data between the two stations. For example, in Figure 10.13, station D keeps track of data packets arriving from three different workstations (B, E, F) on the basis of the virtual circuit number associated with each incoming packet.

## Slide 35: (Circuit vs. Packet Switching)
performance depends on various delays
  propagation delay
    time it takes a signal to propagate between nodes
  transmission time
    time it takes for a transmitter to send a block of data
  node delay
    time it takes for a node to perform processing as it switches data
range of other characteristics, including:
  transparency
  amount of overhead
Notes: Having looked at the internal operation of packet switching, we can now return to a comparison of this technique with circuit switching. IN particular we are concerned with three types of delay:
• Propagation delay: The time it takes a signal to propagate from one node to the next. This time is generally negligible. The speed of electromagnetic signals through a wire medium, for example, is typically 2  108 m/s.
• Transmission time: The time it takes for a transmitter to send out a block of data. For example, it takes 1 s to transmit a 10,000-bit block of data onto a 10-kbps line.
• Node delay: The time it takes for a node to perform the necessary processing as it switches data.
Besides performance, there are a number of other characteristics that may be considered. Stallings DCC9e Table 10.1 summarizes the most important of these, many of which have already been discussed. A few additional comments follow. Circuit switching is essentially a transparent service. Once a connection is established, a constant data rate is provided to the connected stations. This is not the case with packet switching, which typically introduces variable delay, so that data arrive in a choppy manner, or even in a different order than they were transmitted. In addition there is no overhead required to accommodate circuit switching. Once a connection is established, the analog or digital data are passed through, as is. For packet switching, analog data must be converted to digital before transmission; in addition, each packet includes overhead bits, such as the destination address.

## Slide 36: Summary
switched communications networks
  stations / nodes
circuit switching networks
circuit switching concepts
  digital switch, network interfacing, control unit
softswitch architecture
packet switching principles
Notes: Stallings DCC 9e Chapter 10 summary.